# Van’s Aircraft RV-7

# Pilot’s Operating Handbook

PERFORMANCE – SPECIFICATIONS

SPAN: ………………………………………………………………..	25’ 0”

LENGTH: …………………………………………………………….	20’ 4”

HEIGHT:  …………………………………………………………….	5’ 10”

SPEED:

Maximum at Sea Level ……………………………………..	209 mph

Cruise, 75% Power at 8,000 Ft ……………………………..	199 mph

RANGE (includes 3 gal. for taxi, takeoff & climb):

75% @ 8000’ , no reserve .………………………………….	775 sm

55% @ 8000’  no reserve ….……………………………….	950 sm

75% @ 8000’, one hour (10 gal) reserve ……………… Appx 500 sm

55% @ 8000’, one hour (10 gal) reserve ……………… Appx.	680 sm

RATE OF CLIMB AT SEA LEVEL …………………………….….	1,650 FPM

SERVICE CEILING …………………………………………..…….	20,500 FT

TAKEOFF PERFORMANCE: ……………. ……………….………	575 Ft

LANDING PERFORMANCE: ………………..…………….………	500 Ft

STALL SPEED (CAS):

Flaps Up, Power Off ………………………………………	62 mph

Flaps Down, Power Off ……………………………………	58 mph

MAXIMUM WEIGHT (Normal Category): ………………………….	1950 Lbs

EMPTY WEIGHT ………………………………………….		1113 Lbs

MAXIMUM USEFUL LOAD: ……………………………………..	   837Lbs

BAGGAGE ALLOWANCE …………………………………………	  100 Lbs

WING LOADING (Pounds/ Sq. Ft) …………………………………	 14.8 Lbs

POWER LOADING (Pounds/ HP) ………………………………….	 10 Lbs

FUEL:

Capacity ……………………………………………		42 Gal Total

Type ……………………………………………………….	100 LL

OIL CAPACITY …………………………………………………….	8 Qts

ENGINE: Superior/Lycoming…………………………………..XP-IO-360-B1AA2

PROPELLER: Hartzell …………………………………….   	HC-C2YK-1BF

AIRSPEED LIMITATIONS

|  | SPEED | IAS | REMARKS |
| --- | --- | --- | --- |
| VNE | Never Exceed Speed | 230 mph | Do not exceed this speed in any operations. |
| VNO | Maximum Structural Cruising Speed | 193 mph | Exceed this speed only in smooth air. |
| VA | Maneuvering Speed | 142 mph | Do not make full control movements above this speed. Full elevator deflection will result in a 6g load at this speed. |
| VFE | Maximum Flap Extended Speed | 110 –20deg 100 - Full | Do not exceed this speed with flaps down |
| Vy | Best Rate of Climb | 110 mph |  |
| Vx | Best Angle of Climb | 80 mph |  |
| Vs | Stall Speed Clean | 64 mph |  |
| Vso | Stall Speed Landing Configuration | 58 mph |  |

AIRSPEED INDICATOR MARKINGS

| MARKING | IAS VALUE OR RANGE | SIGNIFICANCE |
| --- | --- | --- |
| White Arc | 58-100 mph | Full Flap Operating Range. Lower limit is Vso. Upper limit is maximum speed with flaps extended |
| Green Arc | 64-193 mph | Normal Operating Range. Lower limit is Vs. Upper limit is maximum structural cruising speed |
| Yellow Arc | 193-230 mph | Operations must be conducted with caution and only in smooth air. |
| Red Line | 230 mph | Maximum speed for all operations |

## Views

##### AEROBATIC INFORMATION

Weight Limitation – 1600 Pounds

Recommended Entry Speeds:

Loops, Horizontal Eights 	140-190 mph

Immelman Turns 		150-190 mph

Aileron Rolls, Barrel Rolls 	120-190 mph

Snap Rolls			  80-110 mph

Vertical Rolls 			180-190 mph

Split-S 			100-110 mph

##### PREFLIGHT INSPECTION

1.	CABIN

- Documentation -- Available In Airplane

- Aeronautical Charts – CURRENT AND APPROPRIATE TO FLIGHT

- Seat Belt Securing Control Stick --  RELEASE

- Ignition Switch  -- OFF

- Avionics -- OFF

- Master Switch -- ON

- Engine gages – ON

- Engine tachometer –  RESET FLIGHT TIME

- Fuel Quantity -- CHECK QUANTITY

- Flaps – DOWN

- Master Switch -- OFF

- Alternate Air – IN (Off)

2. EMPENNAGE

- Tail Tie-Down -- DISCONNECT

- Control Surfaces -- CHECK freedom of movement and security

- Static Sources (both sides of fuselage) –CHECK for blockage

- Tail and Strobe--CHECK condition

- Airframe - Condition

3. RIGHT WING

- Aileron -- CHECK freedom of movement and security

- Flap -- CHECK security

- Nav and Strobe--CHECK condition

- Right Landing Light -- CHECK condition

- Wing Tie-Down -- DISCONNECT

- Main Wheel Tire -- CHECK for proper inflation

- Chock -- REMOVE

- Right Wing Tank – SUMP

- Fuel Quantity -- CHECK VISUALLY

Fuel Filler Cap – SECURE

5. NOSE

- Engine Oil Level -- CHECK

- Propeller and Spinner -- CHECK for nicks and security

- Cowl Hinge/Camlocs – CHECK for security

- Air Inlet -- CHECK for restrictions

- Fuel Tank Vents -- CHECK for blockage

6. LEFT WING

- Wing Tie-Down -- DISCONNECT

- Main Wheel Tire -- CHECK for proper inflation

- Chock -- REMOVE

- Left Wing Tank -- SUMP

- Fuel Quantity -- CHECK VISUALLY

- Fuel Filler Cap -- SECURE

- Pitot Tube Cover -- REMOVE and check for blockage

- AOA Ports –Check for blockage Top/Bottom- Drain

- Left Landing Light -- CHECK condition

- Nav and Strobe--CHECK Condition

- Aileron -- CHECK freedom of movement and security

- Flap -- CHECK security

#### BEFORE STARTING ENGINE

- Preflight Inspection -- COMPLETE

- Seat Belts and Shoulder Harnesses -- ADJUST and LOCK

- Fuel Selector Valve -- DESIRED TANK

- Avionics and Electrical -- OFF

- Brakes – AS DESIRED

- Circuit Breakers -- CHECK IN

- Canopy adjust

#### STARTING ENGINE (cold)

- Mixture – Full Rich

- Alternate Air – Push CLOSED

- Master Switch- ON

- Alternator – ON

- Fuel Boost Pump – AS NEEDED

- Throttle - SET to 1/8

- Prop -- HIGH RPM

- Flaps -- UP

- Fuel Boost Pump -- OFF

- Propeller Area -- CLEAR

- Ignition Switch -- START

- Avionics  – ON

- Oil Pressure -- CHECK   25  psi at idle

- Nav & Strobe – ON

### STARTING ENGINE (Warm)

- Mixture -- LEAN

- Throttle to 1/8

- Prop -- HIGH RPM

- Master Switch- ON

- Alternator – ON

- Flaps -- UP

- Propeller Area -- CLEAR

- Ignition Switch – START

- Mixture—Full Rich

- Avionics & Instruments -- ON

- Oil Pressure -- CHECK   25  psi at idle

- Nav & Strobe – ON

BEFORE TAKEOFF

- Brakes -- SET

- Canopy  -------- Main Latch – SECURE

- Flight Controls -- FREE and CORRECT

- Flight Instruments – SET
        	Altimeter – CORRECT PRESSURE
         D/G -- CORRECT HEADING
    		A/H -- ALLIGNED 
        	GPS-- ON

- Fuel Selector Valve -- DESIRED TANK

- Mixture -- RICH (below 3000’)

- Elevator and Aileron Trim -- NEUTRAL

- Throttle -- 1700 RPM

- Magnetos --  CHECK (125 max drop, 50 diff. max)

- Suction – CHECK  (5” Hg)

- Prop – cycle CHECK operation

- Engine Instruments -- CHECK

- Throttle -- IDLE

- Radios -- SET

- Fuel Boost Pump -- ON

- Transponder – ALTITUDE

- Passenger – READY and willing

##### TAKEOFF

#### NORMAL TAKEOFF

- Wing Flaps – UP

- Prop – HIGH RPM

- Throttle --  FULL OPEN

- Elevator Control – AS NEEDED

- Climb Speed --  125 mph

#### SHORT FIELD TAKEOFF

- Wing Flaps – 10 Deg

- Prop – HIGH RPM

- Brakes – APPLY

- Throttle – FULL OPEN

- Mixture – RICH (above 3000’ lean to obtain max RPM)

- Brakes – RELEASE

- Climb Speed – 90mph  (Vy)

##### ENROUTE CLIMB

- Airspeed – 125-150 mph

- Throttle – 25 in Hg, or full throttle

- Prop – 2500 RPM

- Boost Pump – OFF at 1000 feet AGL

- Fuel Pressure – CHECK

- Mixture – LEAN above 5000’

##### CRUISE

- Throttle – 23 in Hg

- Prop – 2300 RPM

- Trim – ADJUST

Mixture – LEAN to 100 deg F rich of peak

##### LANDING

- Approach speed 90 mph

- Flaps 20 deg.

- Prop control full rpm

- Engine 1800 rpm

- 80 mph final

- 40 deg. flaps

##### AFTER LANDING

- Wing Flaps – UP

- Boost Pump – OFF

- Transponder – STANDBY

ENGINE SHUTDOWN

- Flaps – DOWN

- Prop – FULL FORWARD

- Throttle – IDLE

- CHT decidedly dropped

- All electrical sw  – OFF

- Avionics and Instr.-- OFF

- Mixture – IDLE CUT-OFF

- Wait for shut down

- Alternator - OFF

- Master – OFF

#### SECURING AIRCRAFT

- Wheel Chocks

- Wing & Tail Tie-Down

- Pitot Tube Cover

- Cockpit

- Ignition Key – REMOVED

- Master and Electrical Switches – OFF

- Canopy Locked

##### Performance

Cruise Performance at 8,000’:

| MPH | RPM | MAP | Fuel Flow | % Power |
| --- | --- | --- | --- | --- |
| 197 | 2450 | 23” | 10.5 GPH | 75% |
| 187 | 2350 | 22” | 9.5 GPH | 65% |
| 177 | 2250 | 21” | 8.5 GPH | 55% |

No Wind Range at 8,000’:

- All range calculations include 3 gal. for engine start, taxi, takeoff and climb.

- Engine is leaned for best economy.

One hour (10.5 gal.) reserve:

75% Power ………………………………………………..	500 sm

65% Power ………………………………………………..	590 sm

55% Power ………………………………………………..	680 sm

No Reserve:

75% Power ………………………………………………..	700 sm

65% Power ………………………………………………..	790 sm

55% Power ………………………………………………..	880 sm

##### WEIGHT AND BALANCE DATA

Make: Thomas Jones			Model:  RV-7

Serial:    0000			Registration: N4479

Maximum Weights:

Aerobatic Category …………………………	1600 Lbs

Utility Category …………………………….	1700 Lbs

Normal Category ……………………………	1800 Lbs

Datum= 70 inches forward of wing leading edge (L.E.)

Design C.G. Range = 	15% to 29% of wing chord

8.7” to 16.82” from L.E.

78.7” to 86.82” aft of Datum

Wing L.E. = 70 inches aft of datum

Fuel ……………………	80” aft of datum

Pilot and Passenger ……	97.48” aft of datum

Baggage ……………….	126.78” aft of datum

Aircraft weighed empty in level flight attitude.

(Includes 8 qts. of oil, no fuel)

Sample:

Weight		Arm		Moment

Aircraft

Fuel (6lbs/gal)	252		80____	20,160___

Pilot		185		97.48		18,033.80_

Passenger	170		97.48		16,571.60_

Baggage	  76		126.78_	9,635.28__

Total		683				64,400.48_

CG = Total Moment / Total Weight

CG = 	83.68	 in. aft of datum

CG Range = 78.7 to 86.82 inches aft of datum

Empty CG = 79.33      Empty Weight = 1113 lbs.

##### WEIGHT AND BALANCE DATA

| CG Range | 78.7 to 86.82 in aft of datum |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Empty C.G | 78.63 |  |  |  |  |  |  |  |
| Full Fuel/Max Baggage |  |  |  | Standard Pilot/No Baggage/Full Fuel |  |
| Item | Weight | Arm | Moment |  | Item | Weight | Arm | Moment |
| Aircraft | 1,113 | 78.63 | 87515.19 |  | Aircraft | 1,113 | 78.63 | 87515.19 |
| Fuel (6 lbs/gal) | 252 | 80 | 20,160 |  | Fuel (6 lbs/gal) | 252 | 80 | 20,160 |
| Pilot | 210 | 97.48 | 20470.8 |  | Pilot | 170 | 97.48 | 16,571.6 |
| Passenger | 160 | 97.48 | 15596.8 |  | Passenger | 0 | 97.48 | 0 |
| Baggage | 100 | 126.78 | 12678 |  | Baggage | 0 | 126.78 | 0 |
| Total | 1,835 | 85.24 | 156,420.6 |  | Total | 1,535 |  | 124,246.6 |
| CG: | 85.24 |  |  |  | CG: | 80.94 |  |  |
| Zero Fuel CG |  |  |  |  | Zero Fuel CG |  |  |  |
| Heavy Passenger/Max Baggage/ Minimum Fuel |  |  |  | Lightweight Pilot/No Baggage/Full Fuel |  |  |
| Item | Weight | Arm | Moment |  | Item | Weight | Arm | Moment |
| Aircraft | 1,113 | 78.63 | 87515.19 |  | Aircraft | 1,113 | 78.63 | 87515.19 |
| Fuel (6 lbs/gal) | 30 | 80 | 2400 |  | Fuel (6 lbs/gal) | 252 | 80 | 21,160 |
| Pilot | 210 | 97.48 | 20,470.8 |  | Pilot | 100 | 97.48 | 9748 |
| Passenger | 300 | 97.48 | 29,244.0 |  | Passenger | 0 | 97.48 | 0 |
| Baggage | 100 | 126.78 | 12,678.0 |  | Baggage |  | 126.78 |  |
| Total | 1,753 |  | 148,397.9 |  | Total | 1,465 |  | 117,423.0 |
| CG: | 86.88 |  | 152307.9 |  | CG: | 80.15 |  |  |
| Zero Fuel CG |  |  |  |  | Zero Fuel CG |  |  |  |

**CG is .06” aft of aft limit

WEIGHT AND BALANCE DATA - Continued

| Very Heavy Passenger/Max Baggage/ Half Fuel |  |  |  | Very Heavy Passenger/Max Baggage/ Min Fuel |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Item | Weight | Arm | Moment |  | Item | Weight | Arm | Moment |
| Aircraft | 1,113 | 78.63 | 87515.19 |  | Aircraft | 1,113 | 78.63 | 87515.19 |
| Fuel (6 lbs/gal) | 126 | 80 | 10,080 |  | Fuel (6 lbs/gal) | 30 | 80 | 21,160 |
| Pilot | 210 | 97.48 | 20,470.8 |  | Pilot | 210 | 97.48 | 9748 |
| Passenger | 310 | 97.48 | 30,218.8 |  | Passenger | 310 | 97.48 | 0 |
| Baggage | 100 | 126.78 | 12,678.0 |  | Baggage | 100 | 126.78 |  |
| Total | 1,859 |  | 148,397.9 |  | Total | 1,859 | 86.94 | 153282.6 |
| CG: | 86.59 |  | 160,962.6 |  | CG: | 86.94 |  | 153282.6 |
| Zero Fuel CG |  |  |  |  | Zero Fuel CG |  |  |  |

##### **CG is .12” aft of aft limit

##### Engine Information

Model: ……..	Superior/Lycoming XP-IO-360-B1AA2 Fuel Injected

HP: …………	180

Fuel: ………..	91/96 or 100/130 octane minimum

………..	100LL

Oil Filter: …..	Champion CH48110

OIL:  Avg	MIL-L-6082	Ashless Dispersant

Ambiant Air	   Grades		     Grades

Above 80F	SAE 60		      SAE 60,20w50

Above 60F	SAE 60		      SAE 60

30 – 90F		SAE 40		      SAE 40,50

0-70F		SAE 30		      SAE 30,40 or SAE 40

###### Below 10F		SAE 20		      SAE 30 or 20w30

###### Oil Sump Capacity …….. 8 U.S. Quarts

###### Minimum Safe Quantity ...2 U.S. Quarts

###### Operating Conditions:

###### Oil Inlet Temp:		82 deg C desired, 118 deg C Maximum

###### Oil Pressure:		95 psi max; 	 55 psi min; 	 25 psi idle

###### Fuel Pressure:		 ? psi max;	 ? psi min;	 ? psi desired

###### Cyl. Head Temp	66 deg C – 205 deg C desired range,  260 deg C max

###### Max oil consumption .45qts/hr. at cruise

###### Conversion table:

| Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10 | 50 | 60 | 140 | 110 | 230 | 160 | 320 | 210 | 410 |
| 16 | 60 | 66 | 150 | 116 | 240 | 166 | 330 | 216 | 420 |
| 21 | 70 | 71 | 160 | 121 | 250 | 171 | 340 | 221 | 430 |
| 27 | 80 | 77 | 170 | 127 | 260 | 177 | 350 | 227 | 440 |
| 32 | 90 | 82 | 180 | 132 | 270 | 182 | 360 | 232 | 450 |
| 38 | 100 | 88 | 190 | 138 | 280 | 188 | 370 | 238 | 460 |
| 43 | 110 | 93 | 200 | 143 | 290 | 193 | 380 | 243 | 470 |
| 49 | 120 | 99 | 210 | 149 | 300 | 199 | 390 | 249 | 480 |
| 54 | 130 | 104 | 220 | 154 | 310 | 204 | 400 | 254 | 490 |

EMERGENCY PROCEDURES

AIRSPEEDS FOR EMERGENCY OPERATIONS

Engine Failure After Takeoff:

Wing Flaps Up …………………………	90 mph

Wing Flaps Down ……………………..	80 mph

Maneuvering Speed (Va) ……………………….	130 mph

Maximum Glide ………………………………… 	90 mph

ELECTRICAL / ALTERNATOR FAILURE

- Avionics –OFF

- Master Switch – ON

- Alt Toggle  -- OFF

4.    Alt Toggle - ON

IF ALTERNATOR IS STILL OFF-LINE:

- Master Switch – ON

- Electrical Switches – OFF

- Alternator Toggle – OFF

- Avionics – ON as required

- Electrical Equipment – ON, as required

- Flight – TERMINATE as soon as practical, (Aircraft is on battery reserves only!).

EMERGENCY PROCEDURES

ENGINE FAILURES

ENGINE FAILURE DURING TAKEOFF RUN

- Throttle –IDLE

- Brakes – APPLY

- Wing Flaps – RETRACT

- Mixture – IDLE CUT-OFF

- Ignition Switch – OFF

- Master Switch – OFF

ENGINE FAILURE IMMEDIATELY AFTER TAKEOFF

- Airspeed – 80 mph

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Ignition Switch – OFF

- Wing Flaps – AS REQUIRED

- Master Switch – OFF

ENGINE FAILURE DURING FLIGHT

- Airspeed – 90 mph

- Boost Pump – ON

- Fuel Selector – SWITCH TANKS

- Mixture – RICH

- Ignition Switch – BOTH, LEFT, RIGHT

- Transponder – 7700

EMERGENCY PROCEDURES

FIRES

DURING START ON GROUND

- Cranking – CONTINUE, to get a start which would suck the flames and accumulated fuel through the carb and into the engine.

If engine starts:

- Power – 1700 RPM for a few minutes

- Engine – SHUTDOWN and inspect for damage

If engine fails to start:

- Throttle – FULL OPEN

- Mixture – IDLE CUT-OFF

- Cranking – CONTINUE

- Fire Extinguisher – OBTAIN

- Engine – SECURE

ENGINE FIRE IN FLIGHT

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Master Switch – OFF

- Cabin Heat and Air – OFF

ELECTRICAL FIRE IN FLIGHT

- Master Switch – OFF

- Avionics – OFF

- All Other Switches (except ignition) – OFF

- Vents/ Cabin Air/ Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

CABIN FIRE

- Master Switch – OFF

- Vents/ Cabin Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

WING FIRE

- Nav & Strobe Lights – OFF

- Landing Light – OFF

FAR 91.125 - ATC light signals.

ATC light signals have the meaning shown in the following table:

| Color and type of signal | Meaning with respect to aircraft on the surface | Meaning with respect to aircraft in flight |
| --- | --- | --- |
| Steady green | Cleared for takeoff | Cleared to land |
| Flashing green | Cleared to taxi | Return for landing |
| Steady red | Stop | Give way to other aircraft and continue circling. |
| Flashing red | Taxi clear of runway in use | Airport unsafe—do not use |
| Flashing white | Return to starting point on airport | N/A |
| Alternating red and green | Exercise extreme caution | Exercise extreme caution |

## Compass Headings, VFR under 18,000ft

| Course | Altitude |
| --- | --- |
| 0 – 179 degrees | Odd thousand +500 |
| 180 – 360 degrees | Even thousand + 500 |

END